## Slide 1
Induced Seismicity: Fundamentals, New Observations and Outstanding Challenges
William L. Ellsworth
U. S. Geological Survey

## Slide 2
Outline
Earthquake Hazard and Induced Earthquakes
Mechanics of induced earthquakes
Three ongoing case studies
  Paradox Valley, Colorado
  Recent activity near Azle, Texas
  Evolution of Oklahoma seismicity
Think locally, act globally

## Slide 3
Examples of Recent Induced (or Suspected) Earthquakes
Basel, Switzerland (injection for Enhanced Geothermal System)
Lorca, Spain (groundwater withdrawal)
Offshore Valencia, Spain (gas storage)
Groningen, The Netherlands (gas production)
Northern Germany & Southwestern Poland (mining)
Fjallbacka, Sweden (geothermal production)
Blackpool, England (hydraulic fracturing)
Salah, Algeria (CO2 sequestration)
Committee on Induced Seismicity Potential in Energy Technologies, Induced Seismicity Potential in Energy Technologies [National Research Council] (2012).

## Slide 4: What is hazard? How does it differ from risk?
Risk = Hazard  Exposure  Fragility
Risk = Chance of suffering loss or harm
Structural fragility
Non-structural vulnerability
Extent & density of built environment
Faulting, shaking landsliding liquifaction
innundation
Hazard = A source of potential danger or harm

## Slide 5
U. S. Earthquake Hazard Map

## Slide 6: What’s shown on a Hazard Map?
Estimate of earthquake shaking hazard
  Quantified as a probability of strength of shaking in a certain number of years
Primary purpose is to set the seismic design provisions of building codes
U. S. Map update released in July 2014
Update ducked the question of induced earthquakes

## Slide 7: Probabilistic Seismic Hazard Analysis
Where will earthquakes occur in the future?
How often will they happen and how large can they get?
How hard will they shake the ground?
When answers are available for Steps 1-3: Add up all of the sources to find the probability of exceeding damaging shaking.

## Slide 8
Hazard Mapping in the Data-Rich California

## Slide 9
Hazard model for the central and eastern U. S. primarily based on past seismicity
What rate of earthquakes should be expected in the future?

## Slide 10
Higher rate of earthquakes implies higher hazard.
But how much higher?
And where has the hazard increased?
Hazard model for the central and eastern U. S. primarily based on past seismicity

## Slide 11
Increased Earthquake Activity in the U. S. Midcontinent
Higher rate of earthquakes implies higher hazard.
But how much higher?
And where has the hazard increased?
Earthquakes for October, 2014
Magnitude ≥ 2.5

## Slide 12
Rubinstein, J. L., Ellsworth, W. L., McGarr, A., and Benz, H., 2014, The 2001 – Present Triggered Earthquake Sequence in the Raton Basin of Northern New Mexico and Southern Colorado, Bull. Seismol. Soc. Am.
Frohlich, C., 2012, Two-year survey comparing earthquake activity and injection-well locations in the Barnett Shale, Texas. Proc. Natl. Acad. Sci.
Horton, S., 2012, Disposal of Hydrofracking Waste Fluid by Injection into Subsurface Aquifers Triggers Earthquake Swarm in Central Arkansas with Potential for Damaging Earthquake; Seismological Research Letters, v. 83.
W.-Y. Kim, Induced seismicity associated with fluid
injection into a deep well in Youngstown, Ohio.
J. Geophys. Res. 10.1002/jgrb.50247 (2013)

## Slide 13
Induced seismicity presents some formidable challenges as the location of future activity, its duration and magnitude distribution are poorly know at present.
McGarr, 2014, Maximum magnitude earthquakes induced by fluid injection, J. Geophys. Res.
McGarr proposed that the maximum magnitude is limited by the total injected volume.
Kerenan et al. proposed fewer wells were involved in inducing the largest injection-induced earthquake in Oklahoma.
Keranen, K.M., Savage, H.M., Abers, J.A., and Cochran, E.S., 2013, Potentially induced earthquakes in Oklahoma, USA: Links between wastewater injection and the 2011 Mw 5.7 earthquake sequence, Geology., doi:10.1130/G34045.1

## Slide 14
Mw 4.1 January 25,2013 Timpson, Texas Earthquake
55% g
62% g
22 cm/s
Velocity
Mw 4.3 October 2, 2014
Anthony, Kansas Earthquake
70% g
12 cm/s
Progress is being made in determining the ground motion prediction equations from near-source recordings of induced earthquakes.
Velocity
Acceleration
Acceleration

## Slide 15
Mechanics of Induced Earthquakes

## Slide 16
Mechanics of Induced Earthquakes
Bulk Stress Effect

## Slide 17
Gonzales, et al., 2012, The 2011 Lorca earthquake slip distribution controlled by groundwater crustal unloading, Nature, DOI: 10.1038/NGEO1610.
Reverse fault reactivation by unclamping due to groundwater pumping in Lorca, Spain

## Slide 18
Ancient faults can be reactivated by decreasing the effective normal stress
Faults occur on a wide variety of scales and are found in virtually every geologic setting
The Earth’s crust is in a near critical failure state everywhere
Mechanics of Induced Earthquakes
Pore Pressure Effect

## Slide 19
Townend and Zoback, 2001
Critically Stressed Crust
When stress in the crust is in equilibrium with the frictional strength of its faults the maximum differential stress DS is related to the mean stress S by
_
_

## Slide 20
Type equation here.
Hydraulically Conductive Faults in a Near-Critical Stress State

## Slide 21
Increasing the Pore Fluid Pressure May Cause Well-Oriented Faults to Fail
hydroshear regime

## Slide 22
lower hemisphere
stereographic projections
Depth: 1850-2640 m
Hydraulically Conductive Fractures and Faults

## Slide 24
Rocky Mountain Arsenal, Colorado
Earthquake locations by Y. Wang (1965) that led to the discovery of earthquakes induced by wastewater injection at the Rocky Mountain Arsenal. Locations based on regional seismic stations.

## Slide 25
5 km radius
1966
1967
Rocky Mountain Arsenal, Colorado
Diffuse locations of seismicity proved to be an artifact. Well-located events define a vertical fault in Precambrian basement.

## Slide 26
Mw 4.8
“The disposal of waste fluids by injection into a deep well has triggered earthquakes near Denver, Colorado.”
Healy, J.H., Rubey, W.W., Griggs, D.T. and Raleigh, C.B., 1968,
The Denver Earthquakes; Science, v. 161, p. 1301-1310.
Key Points:
High-volume injection into basement
Release of long-stored tectonic stress on ancient faults
Earthquakes occurred more than 10 km from injection point
Largest earthquakes occurred over one year after injection stopped
Earthquakes continued into the 1980s
Injection Volume
Earthquake Count
Rocky Mountain Arsenal, Colorado

## Slide 27
Rocky Mountain Arsenal, Colorado
“The existence of a critical pressure buildup above which earthquakes occur is completely consistent with the theory on the role of fluid pressure in fault movement as presented by Hubbert and Rubey.”

## Slide 28
Raleigh, C.B., Healy, J.H. and Bredehoeft, J.T, 1976, An Experiment in Earthquake Control at Rangely, Colorado; Science, v. 191, p. 1230-1237.
A Test of the Effective Stress Hypothesis at Rangely, Colorado

## Slide 29
“The cessation of seismic activity within 1 day of the initiation of backflow in the experimental wells in May 1973 established the correlation between fluid pressure and earthquakes beyond a reasonable doubt.”
Raleigh, C.B., Healy, J.H. and Bredehoeft, J.T, 1976, An Experiment in Earthquake Control at Rangely, Colorado; Science, v. 191, p. 1230-1237.
A Test of the Effective Stress Hypothesis at Rangely, Colorado
Injection
Backflow
USGS experiment turned-on and off earthquakes in a Colorado oil field by varying injection pressure.
State of stress and pore pressure were measured, as was the frictional strength of the rocks.
Depth (Km)
2
4

## Slide 30
A Test of the Effective Stress Hypothesis at Rangely, Colorado
Injection
Backflow
Depth (Km)
2
4
“Permeability to fluid flow along the fault is sufficiently large that adjustment of fluid pressure in the fault follows rapidly upon changes in fluid pressure at the experimental wells.”
Raleigh, C.B., Healy, J.H. and Bredehoeft, J.T, 1976, An Experiment in Earthquake Control at Rangely, Colorado; Science, v. 191, p. 1230-1237.

## Slide 31: What other processes or initial conditions are important?
Fault slip-enhanced permeability
Rate-and-state nucleation
Spatial heterogeneity in the state of stress
Thermal stresses (cold fluid into hot rock)
Recency of faulting
Chemical processes and fluid-rock interaction
…
McClure and Horne, 2011, Investigation of injection-induced seismicity using a coupled fluid flow and rate/state friction model, Geophysics, doi:10.1190/GEO2011-0064.1

## Slide 32
Gan and Frohlich, 2013, Gas injection may have triggered earthquakes in the Cogdell oil field, Texas, PNAS, doi/10.1073/pnas.1311316110
Under nominally similar conditions why are earthquakes induced in one place but not another?

## Slide 33
Case Study #1: Paradox Valley, Colorado

## Slide 34: U. S. Bureau of Reclamation Paradox Valley Project Saltwater brine extracted from shallow water table below Dolores river is re-injected into limestone at 4.5 km depth
Purpose: Keep salt out of the Colorado River
2CaCO3(s) + Mg++ + SO4--
CaMg(CO3)2(s) + CaSO4(s)
Magnesium in the brine dolomitizes the limestone and precipitates anhydrite
Kharaka, Y. K., et al., 1997, Water Resources Research, v. 33, 1013-1020.
Salt
River
Block, L., et al., 2014, The 24 January 2013 ML 4.4 Earthquake Near Paradox, Colorado and Its Relation to Deep Well Injection, Seismological Res. Lett., v. 85, 609-624.
Notes: http://upload.wikimedia.org/wikipedia/commons/f/f3/Paradox_Valley_Unit_Map.png

## Slide 35
Work of the U. S. Bureau of Reclamation Paradox Valley Unit
Injection Well
Ake, J., et al., 2005, Deep-Injection and Closely Monitored Induced Seismicity at Paradox Valley, Colorado. Bull. Seismological Soc. Am, v. 95, 664-683.
Block, L., et al., 2014, The 24 January 2013 ML 4.4 Earthquake Near Paradox, Colorado and Its Relation to Deep Well Injection, Seismological Res. Lett., v. 85, 609-624.
Pumping History and Seismicity
Notes: Re-drafted Ake et al figure and added the stresses and pressures.
They found that when the injection pressure corrected to 4.3 km depth reached ~80MPa, seismicity began
Only one group of earthquakes fairly close to the well “turned on and off” with the injection pressure.

## Slide 36
µ = 0.83
Effective Normal Stress, MPa
Stresses measured at injection depth of 4.3 km (from minifracs and density log)
State of Stress and Earthquakes at Paradox Valley, CO
First MEQs when borehole fluid pressure at 4.3 km reached 64 to 68 MPa during Injection Test #1 (11,000 m3 in 13 days), close to predicted threshold of P = 61 MPa.
ΔP = 17 Mpa
(P = 61 MPa)
Most earthquakes then occurred during large-volume injection associated with primary brine disposal (avg. P = 81.4 MPa > Shmin)
P = 81.4 MPa
Pre-injection fluid pressure
(P = 43.6 MPa)
Sv (≤ σ1)
Shmin
Ake, J., et al., 2005, Deep-Injection and Closely Monitored Induced Seismicity at Paradox Valley, Colorado. Bull. Seismo. Soc. Am, v. 95, 664-683.
Notes: Re-drafted Ake et al figure and added the stresses and pressures.
They found that when the injection pressure corrected to 4.3 km depth reached ~80MPa, seismicity began
Only one group of earthquakes fairly close to the well “turned on and off” with the injection pressure.

## Slide 37
Case Study #2: Azle Texas
2

## Slide 38
Azle Texas earthquakes of November 2013 – January 2014

## Slide 39
Routine USGS/NEIC Locations
20 Km

## Slide 40
Temporary Network Locations
Earthquakes hypocenters define a northwest dipping normal fault in the shallow basement (3.5 to 7 km)

## Slide 41
Faults, Seismicity and Wells

## Slide 42
Earthquake Swarm of January 28, 2014
Double-difference waveform cross correlation locations
Courtesy of David Shelly

## Slide 43
Why Earthquakes Near Azle?
Natural earthquake activity?
Water level changes in Eagle Mountain Lake?
Water table decline due to prolonged drought?
Production from the Barnett Shale?
Waste water disposal?

## Slide 44
Could Lake Level Changes Have Induced the Earthquakes?
Compute stress change at depth using the Boussinesq solution for a surface load. Maximum change in focal region < 1 KPa.

## Slide 45
Barnett Shale Production?

## Slide 46
Wastewater Disposal?
High-volume wastewater disposal wells

## Slide 47
Causal Factors for Seismicity near Azle, Texas
Matthew J. Hornbach, Heather R. DeShon, William L. Ellsworth, Brian Stump, Chris Hayward, Harrison R.Oldham, Cliff Frohlich, Jon E. Olson, M. Beatrice Magnani, Casey Brokaw, James H. Luetgert.
Nature Communications, in review.
Modeling the Effects of Injection and Production
Solve the groundwater-flow equation for pressure assuming single phase flow and nearly flat-lying sedimentary layers, where
where S is the specific storage and is the hydraulic conductivity and G is the source term.

## Slide 48
Causal Factors for Seismicity near Azle, Texas
Matthew J. Hornbach, Heather R. DeShon, William L. Ellsworth, Brian Stump, Chris Hayward, Harrison R.Oldham, Cliff Frohlich, Jon E. Olson, M. Beatrice Magnani, Casey Brokaw, James H. Luetgert.
Nature Communications, in review.

## Slide 49
Evidence For or Against Proposed Mechanisms
Potential Cause | Arguments For | Arguments Against
Natural | Rare earthquakes do occur in Texas and history is short | Earthquakes in this region unknown for >100 years
Lake Level Change | Falling lake level reduces load on footwall | Stress changes from falling lake level are too small(< 1 KPa)
Production | Poroelastic stress changes would encourage normal faults to failure | Poroelastic stress changes are smaller than production pressure decrease
Injection | Pressure increase at fault in range seen for natural triggering | Unclear how pressure is transmitted into basement

## Slide 50
Case Study #3: Oklahoma

## Slide 52
SandRidge Energy
Earthquakes in north-central Oklahoma (and southern Kansas) initiate within about a year of drilling to develop shale oil resources

## Slide 53: Fracking or Wastewater Disposal?
Hundreds of thousands of frac jobs in the U.S.
Only a handful of felt events.
None as large as magnitude 3 have been documented in the U.S.
Mw 4.2 in Canada
30,000 deep wastewater wells in U.S.
Many with volumes > 106 m3
Few with detected seismicity
Magnitudes as large as Mw 5.7
Notes: Hydraulic fracturing is used to increase the permeability of shales or coal seams so as to produce natural gas. These wells also produce formation brines and fracking compounds that are usually disposed by injection down deep wells.

## Slide 54
1970 - 1979
P(one or more) = 1 – exp(-(Annual Rate) t)

## Slide 55
1980 - 1989

## Slide 56
1990 - 1999

## Slide 57
2000 - 2008

## Slide 58
2009 - 2013
New Ways of Extracting Oil from Previously Unproductive Formations

## Slide 59
Example of the Hunton Dewatering Play
Water to oil ratio at start:
1:50
When economical:
15:1

## Slide 60
Central Oklahoma “Jones” Swarm
2009-2011
million m3
Year
Oklahoma City Injection
25 Km
Injection Wells
(area ~ annual volume)
Sharp increase in central Oklahoma seismicity 2009-2014 induced by massive wastewater injection. K. M. Keranen, M. Weingarten, G.A. Abers, B. A. Bekins, S. Ge
Science, 2014.

## Slide 61
2009 - 2013
2011Mw 5.7 Prague, OK
Wells
Keranen, K.M., Savage, H.M., Abers, J.A., and Cochran, E.S., 2013, Potentially induced earthquakes in Oklahoma, USA: Links between wastewater injection and the 2011 Mw 5.7 earthquake sequence, Geology., doi:10.1130/G34045.1

## Slide 62
2014 through May
P(M≥5½) = 0.23 to 0.53
in the next 12 months
Compared with the 1970-2008 expectation of
P(M≥5½) = 0.003

## Slide 63
Oklahoma Seismicity 1973 - 2014
Oklahoma and California Earthquake Rate for Sequences with at least one M ≥ 3
Oklahoma
California

## Slide 64
Five Candidate Logic Tree Branches
Branch 1: Short-Term Variability in a Long-Term Background EQ Rate
Branch 2: Seismicity Rate Change is the “New Normal”
Branch 3: New EQs Come From a New, Distinct EQ Population
Branch 4: Increase is transient
Branch 0: No change in underlying Long-Term Background EQ Rate
Model used in the 2014 update to hazard map
(2% in 50 years)
Earthquake rate is not stationary and so Poisson model is hard to justify
Extrapolation of current rate for 50 years in question
Uncertain how to justify choice of new maximum magnitude (Mmax)
Model assumes knowledge of end of activity and decay rate
Mmax

## Slide 65
Content is preliminary and should not be considered a final USGS product.
Branch 3: New EQs Come From
a New, Distinct EQ Population
Base Case: Ignore Increased Earthquake Rate

## Slide 66
Content is preliminary and should not be considered a final USGS product.
1 Hz, 02px50 |  |  |  |  | 
 | No SFI base-case | SFI Mmax=6 | Ratio Mmax6/bc | SFI Mmax=7 | Ratio Mmax7/bc
Wichita | 0.024 | 0.033 | 1.4 | 0.055 | 2.3
Austin | 0.013 | 0.019 | 1.5 | 0.027 | 2.1
Oklahoma City | 0.044 | 0.226 | 5.1 | 0.406 | 9.2
1 Hz hazard (2% in 50 yrs) from seismicity only (2008 GMPEs)
Branch 3: New EQs Come From
a New, Distinct EQ Population

## Slide 67
2011 Prague, Oklahoma Earthquake
Mw 5.7
No fatalities; a few injuries; moderate economic damage
Think Locally, Act Globally

## Slide 68
2011 Prague, Oklahoma Earthquake
Mw 5.7
No fatalities; a few injuries; moderate economic damage
Think Locally, Act Globally
1986 San Salvador Earthquake
Mw 5.7
1500 fatalities; 10,000 injuries;
100,000 homeless

## Slide 69
Think Locally, Act Globally

## Slide 70
We currently have very limited predictive capability due to:
  Uncertainty in the stress state and pore pressure
  Rudimentary knowledge of flow paths
  Poor knowledge of potentially capable faults
  Poor detection and location capabilities of seismic networks
  Difficulty in predicting how large an earthquake will grow once initiated
  Uncertainty in the expected strength of shaking
  Uncertainty in the physical model(s) used to describe the system
Where do we go from here?

## Slide 71
Thank you

## Slide 72
Chart: 
| Fracking | Enhanced Oil Reovery | Enhanced Geothermal | Production | Surface Reservoir | Injection
Column2 | 0 | 0 | 0 | 0 | 0 | 0
Common | 2 | 3 | 1 | 2 | 3 | 3
Rare | 2.2 | 1.8 | 2.5 | 5 | 4.8 | 2.6
Magnitude
“Magnitude Range” of Earthquakes Induced
by Different Anthropogenic Sources

## Slide 73: How well does the 2008 map forecast 2009-2012 seismicity?
How many earthquakes were expected to occur in 2009 – 2012?
How many earthquakes did occur?
How likely was it that the differences were by chance?

## Slide 74: Smoothed Seismicity “NSHM08 a-values”
Induced earthquakes removed in polygons

## Slide 75: Declustered Earthquakes 2009-2013

## Slide 76: P(Nobs|NSHM): 2009-2013
Content is preliminary and should not be considered a final USGS product.
Notes: Cogdell (p~0.01)

## Slide 77
July 2014 Update to the U. S. National Seismic Hazard Map
How should we account for the increased seismicity?